IMX8MP-SOM-xGB-IND

User Manual

Document revision 2.0 www.olimex.com
# iMX8MP-SOM-4GB-IND board features

iMX8MP-SOM-4GB-IND exposes all MIMX8ML8CVNKZAB GPIOs and features in a very compact format. It takes care for power supply and high speed memory signals complexities.

- MIMX8ML8CVNKZAB Quad core Cortex-A53 @1600Mhz + Arm Cortex-M7 @800 Mhz
- 4GB LPDDR4 RAM
- PMIC PCA9450
- 24 Mhz crystal
- 32.768 kHz crystal
- EEPROM memory (for Linux configuration or settings)
- Power LED
- User LED
- 5 x 40 pin + 1 x 20 pin total 220 pin connectors with 1.27 mm/0.05" step
- LVDS, 2 x MIPI CSI, MIPI DSI ribbon connectors on top
- Extended operating temperature – from -20°C to +85°C
- Dimensions: (70 x 43)mm
- 4 holes for mounting
- Open source hardware design, all KiCAD design files available for download

Compatible with iMX8MP-SOM-EVB-IND – iMX8MP-SOM-4GB-IND can be placed on top of expansion board for easier R&D and prototyping.
# MIMX8ML8CVNKZAB chip features

The main chip has the following features:
- MIMX8ML8CVNKZAB Quad core Cortex-A53 @1600Mhz + Arm Cortex-M7 @800 Mhz
- 512KB Cache
- Vivante GC520L, Vivante GC7000UL
- HDMI HD1080p60 H.264, HD1080p60 H.265, VP8 video codec, VP9 video codec
- MIPI-DSI
- LVDS 4/8 lanes
- NPU 2.3 TOPS
- 2 x Gigabit Ethernet (1 x TSN)
- 2 x MIPI-CSI camera
- 1 x ISP camera
- 2 x USB3 with OTG
- 1 x PCIe 3.0
- 2 x CAN FD
- 3 x SPI
- 5 x I2C
- 3 x SDIO eMMC 5.1
- 4 x UART 5Mbit
- 4 x PWM
- Audio: ASRC, HiFi 4 DSP, SAI/I2S, eARC
# iMX8MP-SOM-EVB-IND board of peripherals features

iMX8MP-SOM-EVB-IND can be placed on top of expansion board for easier R&D and prototyping. It has the following features:

- iMX8MP-SOM matching connectors
- Two Gigabit Ethernet connectors
- Two CAN transceivers
- HDMI
- Power jack 5V
- UEXT connector
- Two GPIO connectors
- Two serial debug UARTs (for A53 and M7)
- Optional ARM JTAG connector
- Micro SD-card connector
- Flash module connector
- USB 3 hosts
- Headphone 3.5mm connector
- Microphone 3.5 mm connector
- Reset button
- PWR button
- Boot slide switch
- Industrial grade temeprature range: (-45+85)C
- Dimensions: (155 x 102)mm
## Order codes for iMX8MP-SOM and accessories

iMX8MP-SOM-4GB-IND	Main module with iMX8MPLUS, 4GB LPDDR4, EEPROM, PMIC
iMX8MP-SOM-EVB	Evaluation board with peripherals that can be used as a reference	design, compatible with iMX8MP-SOM-4GB-IND
MICRO-SD-16GB-CLASS10	Blank 16GB microSD card
SY1005E	Power adapter 5V 2A
USB-SERIAL-F	Serial debug cable for console log
CABLE-HDMI-50CM	HDMI cable
BATTERY-LIPO1400mAh	Li-Po battery for standalone operation
LCD/LCD-OLinuXino-5CTS	5 inch LCD 800x480 pixels with capacities touch panel
LCD-OLinuXino-7CTS	7 inch LCD 1024x600 pixels with capacitive touch panel
LCD-OLinuXino-10CTS	10 inch LCD 1024x600 pixels with capacitive touch panel
UEXT modules	Expansion modules temperature, humidity, pressure, magnetic field,	light sensors. Modules with LCDs, LED matrix, Relays, Bluetooth,	Zigbee, WiFi, GSM, GPS, RFID, RTC, EKG, sensors and etc.
# HARDWARE
## iMX8MP-SOM layout

MIMX8ML8CVNKZAB
32Gb LPDDR4
Orientation mark

MIPI-CSI2
LCD LVDS
MIPI-CSI1
MIPI-DSI

EEPROM
GPIO2
GPIO3

PMIC
GPIO1
GPIO6
GPIO5
GPIO4

GPIO3
GPIO2

## iMX8MP-SOM schematics

iMX8MP-SOM-4GB-IND latest schematic is at our GitHub.

Hardware sources and more can also be found here:

https://github.com/OLIMEX/iMX8MP-SOM/tree/main/HARDWARE
## iMX8MP-SOM connectors
### GPIO1

### GPIO2

### GPIO3

### GPIO4

### GPIO5

### GPIO6
### LCD

### MIPI-DSI

### MIPI-CSI
### EEPROM
### User LED

# SOFTWARE

Olimex provides buildroot for the board that can be found here:

https://images.olimex.com/release/imx8mp/
# Document Revision History
Revision 2.0 December 2024
- Improved formatting
- Fixed wrong info about Linux available
Revision 1.0 May 2024
- Initial document