iMX8MP-SOM-xGB-IND
User Manual
Rev.1.0 May 2024	olimex.com
# What is iMX8MP-SOM-xGB-SOM

iMX8MP-SOM-4GB-IND is system on module development board with
- MIMX8ML8CVNKZAB Quad core Cortex-A53 @1600Mhz + Arm Cortex-M7 @800 Mhz
- 512KB Cache
- Vivante GC520L,Vivante GC7000UL
- HDMI HD1080p60 H.264,HD1080p60 H.265,VP8 video codec,VP9 video codec
- MIPI-DSI
- LVDS 4/8 lanes
- LPDDR4
- PMIC
- NPU 2.3 TOPS
- 2 x Gigabit Ethernet (1 x TSN)
- 2 x MIPI-CSI camera
- 1 x ISP camera
- 2 x USB3 with OTG
- 1 x PCIe 3.0
- 2 x CAN FD
- 3 x SPI
- 5 x I2C
- 3 x SDIO eMMC 5.1
- 4 x UART 5Mbit
- 4 x PWM
- Audio: ASRC,HiFi 4 DSP,SAI/I2S,eARC
# iMX8MP-SOM features:

iMX8MP-SOM-4GB-IND exposes all MIMX8ML8CVNKZAB GPIOs and features in very compact format. It takes care for power supply and high speed memory signals complexities.

- MIMX8ML8CVNKZAB Quad core Cortex-A53 @1600Mhz + Arm Cortex-M7 @800 Mhz
- 4GB LPDDR4 RAM
- PMIC PCA9450
- 24 Mhz crystal
- 32.768 kHz crystal
- Linux configuration EEPROM
- Power LED
- User LED
- 5x 40 pin + 1x 20 pin total 220 pin connectors with 1.27 mm/0.05" step
- Operating temperature -20+85C
- Dimensions: 70 x 43 mm

## Order codes for iMX8MP-SOM and accessories:

iMX8MP-SOM-4GB-IND	module with iMX8MPLUS, 4GB LPDDR4, EEPROM, PMIC
iMX8MP-SOM-EVB	evaluation board for iMX8MP-SOM which can be used	as reference design
MICRO-SD-16GB-CLASS10	16GB microSD card
SY1005E	power adapter 5V 2A
USB-SERIAL-F	serial debug cable for console log
CABLE-HDMI-50CM	HDMI cable
BATTERY-LIPO1400mAh	LiPo battery for standalone operation
LCD/LCD-OLinuXino-5CTS	5 inch LCD 800x480 pixels with capacitive touch panel
LCD-OLinuXino-7CTS	7 inch LCD 1024x600 pixels with capacitive touch panel
LCD-OLinuXino-10CTS	10 inch LCD 1024x600 pixels with capacitive touch panel
UEXT modules	There are temperature, humidity, pressure, magnetic field, light sensors.	Modules with LCDs, LED matrix, Relays, Bluetooth, Zigbee, WiFi,	GSM, GPS, RFID, RTC, EKG, sensors and etc.
# HARDWARE

## iMX8MP-SOM layout:

MIMX8ML8CVNKZAB
32Gb LPDDR4
Orientation mark

MIPI-CSI2
LCD LVDS
MIPI-CSI1
MIPI-DSI

GPIO5
GPIO6
GPIO4
GPIO3
GPIO2
PMIC
GPIO1
EEPROM
## iMX8MP-SOM schematics:

iMX8MP-SOM-4GB-IND latest schematic is on Olimex web.

## iMX8MP-SOM connectors:
### GPIO1

### GPIO2
### GPIO3
### GPIO4
### GPIO5
### GPIO6

### LCD
### MIPI-DSI
## MIPI-CSI

## EEPROM
## User LED

# SOFTWARE

# Recommended Olimage Linux images and changelog
# Olimage Linux guide
# Revision History
Revision 1.0 May 2024	initial